FIRA Robot World Cup 2026
Mission Impossible Foresight

Maze Runner

Introduction
The Mission Impossible Foresight – Maze Runner - is a game, where a robot has to first explore a small maze and then find the fastest path to escape the maze.
Robot
The size of the robot is limited to a square of size 216mm (i.e., the shorter side of a letter sized sheet of paper).
The robot must move fully autonomously.
Maze
The maze consists of lines taped on a background of sufficient contrast (e.g., a black line on a white surface or vice versa).
The maze consists of eight squares or rectangles with a side length of approximately 30cm.
P / Q / R1 / R2 / Trap sprung / Trap ok / Trap for U19 only / Row 7 / Row 8 / Row 9 / Row 11 / Row 10 / Row 12 / Row 1 / Row 2 / Row 3 / Row 4 / Row 5 / Row 6
Fig 1: Maze with some traps (Red). Robot R1’s sensor touches the trap, but its center is not on top – so R1 is ok. The center of the robot R2 is over the trap and hence the trap is sprung.

Traps
A path can be blocked by a trap, that is a red square with a length of approximately 5cm, which can be placed on top of a line.
A trap is sprung if the projection of the center of the robot onto the playing surface is on top of the trap. In other words, the robot can use a light sensor or camera to scan the line ahead, but then must stop and turn around before the center of the robot touches the trap.
See Fig. 1 above for an example, where robot R1 is still legal, but R2 has sprung the trap.
In the U14 category, all traps fwill be placed on the vertical lines of the field. In the U19 category, the traps can be placed on any field line.
Gameplay
First the referee will toss a coin to determine the start location of the robot (point P or Q). The robot handler must place the robot at the start point.
After the referee gives the start signal (e.g., blows the whistle), the robot handler is allowed to quickly start the robot by pressing a button. After this, the handler is not allowed to interact with the robot in any way (e.g., hand signals, sound, touching).
The robot must follow the maze lines, that is at least part of the robot’s projection onto the playing field must intersect with a field line at all times. If the robot left the line, then the round will be terminated.
If the robot springs a trap, then the round will be terminated.
After the robot has started moving, the referee will randomly place the traps in the maze. The placement will be randomized in such a way that the total length of the optimal path from Start (P or Q) to Finish (Q or P) will be the same for all robots in a single round.
There are two phases to the competition: exploration and speed run. During the exploration phase, the robot must find a path from Start to Finish. After the robot’s sensor touches the Finish point for the first time, the speed run phase will start.
The goal of the speed run phase is to reach the original Start point as quickly as possible. The referee will start a timer. The referee will stop the timer when the robot reaches the original start point without any infractions.
The maximum duration of each round (exploration plus speed run) is 2 min.
Scoring
Teams that are able to finish the run without infractions will be ranked by the time of their speed run. In case of a tie, the time of the exploration run will be used as a time breaker.
Teams that are penalized for an infraction will be ranked based on the row where the infraction occurred. There are six rows, Row 1 to row 6 for the exploration phase and row 7 to row 12 for the speed run phase. In the figure above, R2 sprung the trap during the speed run phase, and hence will be scored as Row 10.
If the robot’s projection is into two different rows (e.g., row 5 and 6) when the infraction occurred then the lower numbered row will be used as the point of the infraction (e.g., row 5).
For robots that committed an infraction, the row will be used to rank the teams. In case, of a tie, the time until the infraction will be used.
Failure to follow the instructions of the referee or other unsportsmanlike behavior will lead to disqualification.